## Slide 1
DHCPv6 and
IPv6 Automatic Address Allocation
Cisco Networking Academy
Rick Graziani
CS/CIS Instructor
Cabrillo College

## Slide 2: Agenda
DHCPv4 – Remember IPv4?
ICMPv6 – Used more than ICMPv4
SLAACers – IPv6 Addressing without DHCPv6
Stateless DHCPv6 – I have my address but need some other stuff
Stateful DHCPv6 – Just like DHCPv4 (only different)

## Slide 3: DHCPv4 – Remember IPv4?

## Slide 4: IPv4 Dynamic Addresses
DHCP Server
Client decides to use DHCPv4.

## Slide 6: ICMPv6 – Used more than ICMPv4

## Slide 7: Internet Control Message Protocol (ICMPv6)
Described in RFC 4443
Much more robust than ICMP for IPv4
Contains new functionality and improvements.
More than just “messaging” but “how IPv6 conducts business”.
General message similar to ICMP for IPv4
Also uses Type and Code fields like in ICMPv4.
Two types of ICMPv6 messages
  Error messages
  Informational messages

## Slide 8: Neighbor Discovery Protocol Uses ICMPv6
ICMPv6 informational messages used by Neighbor Discovery (RFC 4861):
  Router Solicitation Message
  Router Advertisement Message
  Neighbor Solicitation Message
  Neighbor Advertisement Message
  Redirect Message (Similar to ICMPv4)
Router-Device Messaging
Device-Device Messaging

## Slide 9: SLAACers – IPv6 Addressing without DHCPv6

## Slide 10: Configuring Dynamic IPv6 Addresses
Global Unicast
Manual
IPv6 Unnumbered
IPv6 Address
Stateless Autoconfiguration
DHCPv6
Static
EUI-64
Dynamic

## Slide 11: IPv6 – It all begins with the Router Advertisement
The Router Solicitation message is used to ask, “How to I I obtain an IPv6 address automatically?”
I need IPv6 address information…
I need IPv6 addressing information….
Let me tell you how we’re going to do this….

## Slide 12: With IPv6 it begins with the Router Advertisement
The Router Advertisement (RA) tells hosts how it will receive IPv6 Address Information.
Sent periodically by an IPv6 router or…
When the router receives a Router Solicitation message from a host.

## Slide 13: A Router Must Be Enabled as an “IPv6 Router”
Router Advertisement/Solicitation Messages
Part of ICMPv6 (Internet Control Message Protocol for IPv6)
Router Advertisements are sent by an “IPv6 router” – ipv6 unicast-routing command
  Forwards IPv6 Packets
  Can be enabled for IPv6 static and dynamic routing
  Sends ICMPv6 Router Advertisements
Routers can be configured with IPv6 addresses without being an IPv6 router
DHCPv6 Server
R1(config)# ipv6 unicast-routing

## Slide 14: SLAAC (Stateless Address Autoconfiguration)
DHCPv6 Server
R1(config)# ipv6 unicast-routing
Option 1 (Default on Cisco routers) O Flag = 0, M Flag = 0
“I’m everything you need (Prefix, Prefix-length, Default Gateway)”
Option 2 (Discussed in CCNA Switching) O Flag = 1, M Flag = 0
“Here is my information but you need to get other information such as DNS addresses from a DHCPv6 server.”
Option 3 (Discussed in CCNA Switching) O Flag = x, M Flag = 1
“I can’t help you. Ask a DHCPv6 server for all your information.”
RA
DHCPv6
Option 1 and 2: Stateless Address Autconfiguration – DHCPv6 Server does not maintain state of addresses
Option 3: Stateful Address Configuration – Address received from DHCPv6 Server

## Slide 15: SLAAC

## Slide 16: Router Advertisement – Option 1
Option 1 – RA Message
To: FF02::1 (All IPv6 devices multicast)
From: FE80::1 (Link-local address)
Prefix: 2001:DB8:ACAD:1::
Prefix-length: /64
RA
1
MAC: 00-03-6B-8C-E0-80
Prefix: 2001:DB8:ACAD:1::
Prefix-length: /64
Default Gateway: FE80::1
Global Unicast Address:
2001:DB8:ACAD:1: + Interface ID
2001:DB8:ACAD:1::/64
EUI-64 Process or Random 64-bit value
2
DHCPv6 Server
3

## Slide 17: Dynamic Interface ID
Interface ID
Subnet ID
Global Routing Prefix
/48
/64
64 bits
EUI-64 Process
Randomly Generated Number
SLAAC
Router Advertisement
2001:DB8:ACAD:1::/64
Windows operating systems, Windows XP and Server 2003 use EUI-64.
Windows Vista and newer; hosts create a random 64-bit Interface ID.
Linux: Mostly use random 64-bit number
Mac OSX: use EUI-64 (on my Macs)
DHCPv6 Server

## Slide 18: EUI-64 (Extended Unique Identifier – 64)
Option 1 – RA Message
To: FF02::1 (All-hosts multicast)
From: FE80::1 (Link-local address)
Prefix: 2001:DB8:ACAD:1::
Prefix-length: /64
RA
1
MAC: 00-03-6B-E9-D4-80
Prefix: 2001:DB8:ACAD:1::
Prefix-length: /64
Default Gateway: FE80::1
Global Unicast Address:
2001:DB8:ACAD:1: + Interface ID
2001:DB8:ACAD:1::/64
EUI-64 Process or Random 64-bit value
2
DHCPv6 Server

## Slide 19: EUI-64
Hexadecimal
OUI
24 bits
Device Identifier
24 bits
Binary
Step 1: Split the MAC address
Binary
Step 2: Insert FFFE
Binary
Step 3: Flip the U/L bit
Binary
Modified EUI-64 Interface ID in Hexadecimal Notation
1111 1111
1111 1110
1111 1111
1111 1110
02
03
6B
E9
D4
80
FF
FE
00
03
6B
E9
D4
80
0000 0000
0000 0011
0110 1011
1110 1001
1101 0100
1000 0000
1110 1001
1101 0100
1000 0000
1110 1001
1101 0100
1000 0000
0000 0000
0000 0011
0110 1011
0000 0010
0000 0011
0110 1011
F F F E

## Slide 20
PC1> ipconfig
Windows IP Configuration
Ethernet adapter Local Area Connection:
Connection-specific DNS Suffix . :
IPv6 Address. . . . . . . . . . . : 2001:db8:acad:1:02-03-6b-ff-fe-e9-d4-80
Link-local IPv6 Address . . . . . : fe80::02-03-6b-ff-fe-e9-d4-80
Default Gateway . . . . . . . . . : fe80::1
PC1: Global Unicast Address
A 64-bit Interface ID and the EUI-64 process accommodate the IEEE specification for a 64-bit MAC address.
Router Advertisement
EUI-64
Why a 64-bit interface ID?

## Slide 21: Stateless DHCPv6 – I have my address but need some other stuff

## Slide 22: Configuring Dynamic IPv6 Addresses
Global Unicast
Manual
IPv6 Unnumbered
IPv6 Address
Stateless Autoconfiguration
DHCPv6
Static
EUI-64
Dynamic

## Slide 23: Stateless DHCPv6
DHCPv6 Server
R1(config)# ipv6 unicast-routing
Option 1 (Default on Cisco routers) O Flag = 0, M Flag = 0
“I’m everything you need (Prefix, Prefix-length, Default Gateway)”
Option 2 (Discussed in CCNA Switching) O Flag = 1, M Flag = 0
“Here is my information but you need to get other information such as DNS addresses from a DHCPv6 server.”
Option 3 (Discussed in CCNA Switching) O Flag = x, M Flag = 1
“I can’t help you. Ask a DHCPv6 server for all your information.”
RA
DHCPv6
Option 1 and 2: Stateless Address Autconfiguration – DHCPv6 Server does not maintain state of addresses
Option 3: Stateful Address Configuration – Address received from DHCPv6 Server

## Slide 24: Stateless DHCPv6
DHCPv6
The Router Advertisement’s Other Configuration Flag is set to “1” meaning, use me for your address but you need to get other information from a DHCPv6 server.
DHCPv6 Server
O Flag = 1, M Flag = 0
I created my own address,
have a prefix-length, default gateway, but I need a DNS address…
R1(config)# interface g0/0
R1(config-if)# ipv6 nd other-config-flag

## Slide 25: Cisco Router Stateless DHCPv6 Server
DHCPv6
O Flag = 1, M Flag = 0
I created my own address,
have a prefix-length, default gateway, but I need a DNS address…
DHCPv6 Server
SOLICIT To all DHCPv6 Servers
3
ADVERTISE Unicast
REQUEST or INFORMATION REQUEST Unicast
REPLY Unicast
4
5
6

## Slide 26: Configuring Stateless DHCPv6
Notice there isn’t a client IPv6 address

## Slide 27
DHCPv6 Server
2607:F380:80F:F828::/64
G0/0
G0/01
2607:F380:80F:F830::/64
Cabrillo College 2607:F380:80F::/48
CS/CIS Department 2607:F380:80F:Fxxx::/64
xxx = VLAN/Room
Classroom 828
Lab Room 830
Stateless DHCPv6
Stateful
DHCPv6

## Slide 28
DHCPv6 Server
Router(config)# ipv6 unicast-routing
Router(config)# ipv6 dhcp pool IPV6-STATELESS
Router(config-dhcpv6)# dns-server 2607:F380:80F:F425::252
Router(config-dhcpv6)# dns-server 2607:F380:80F:F425::253
Router(config-dhcpv6)# domain-name cis.cabrillo.edu
Router(config)# interface GigabitEthernet 0/0
Router(config-if)# ip address 172.30.1.1 255.255.255.0
Router(config-if)# ipv6 address FE80::F828:1 link-local
Router(config-if)# ipv6 address 2607:F380:80F:F828::1/64
Router(config-if)# ipv6 nd other-config-flag
Router(config-if)# ipv6 dhcp server IPV6-STATELESS
2607:F380:80F:F828::/64
Router Advertisement O=1
DHCPv6 Solicit
DHCPv6 Advertise
I created my own address,
have a prefix-length, default gateway, but I need a DNS address…
G0/0
S
T
A
T
E
L
E
S
S
D
H
C
P
v
6
Now I have a DNS address and a domain!

## Slide 29
Stateless DHCPv6 Server
C:\Users\Student>ipconfig /all
Windows IP Configuration
Ethernet adapter Local Area Connection:
Description . . . . . . . . . . . : Intel(R) 82566DM-2 Gigabit Network Connection
Physical Address. . . . . . . . . : 00-21-9B-88-0E-40
DHCP Enabled. . . . . . . . . . . : No
Autoconfiguration Enabled . . . . : Yes
IPv6 Address. . . . . . . . . . . : 2607:f380:80f:f828:6909:cb1c:36a0:a595
IPv4 Address. . . . . . . . . . . : 192.168.1.10(Preferred)
Subnet Mask . . . . . . . . . . . : 255.255.255.0
Default Gateway . . . . . . . . . : fe80::f828:1
DNS Servers . . . . . . . . . . . : 2607:f380:80f:f425::252
2607:f380:80f:f425::253
Connection-specific DNS Suffix Search List: cis.cabrillo.edu
2607:F380:80F:F828::/64
Router Advertisement
Stateless DHCPv6
2607:f380:80f:f828:6909:cb1c:36a0:a595
G0/0

## Slide 30
Stateless DHCPv6 Server
Router# show ipv6 interface g 0/0
GigabitEthernet 0/0 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::F828:1
Description: === Classroom-828 network
Global unicast address(es):
2607:F380:80F:F828::1, subnet is 2607:F380:80F:F828::/64
<Output omitted>
Hosts use stateless autoconfig for addresses.
Hosts use DHCP to obtain other configuration.
Router#
2607:F380:80F:F828::/64
2607:f380:80f:f828:6909:cb1c:36a0:a595
G0/0

## Slide 31: Stateful DHCPv6 – Just like DHCPv4 (only different)

## Slide 32: Stateful DHCPv6
DHCPv6 Server
R1(config)# ipv6 unicast-routing
Option 1 (Default on Cisco routers) O Flag = 0, M Flag = 0
“I’m everything you need (Prefix, Prefix-length, Default Gateway)”
Option 2 (Discussed in CCNA Switching) O Flag = 1, M Flag = 0
“Here is my information but you need to get other information such as DNS addresses from a DHCPv6 server.”
Option 3 (Discussed in CCNA Switching) O Flag = x, M Flag = 1
“I can’t help you. Ask a DHCPv6 server for all your information.”
RA
DHCPv6
Option 1 and 2: Stateless Address Autconfiguration – DHCPv6 Server does not maintain state of addresses
Option 3: Stateful Address Configuration – Address received from DHCPv6 Server

## Slide 33: Stateful DHCPv6
DHCPv6
The Router Advertisement’s Managed Configuration Flag is set to “1” meaning, the client needs to get ALL of it’s information from a DHCPv6 server.
DHCPv6 Server
O Flag = x, M Flag = 1
The router’s Router Advertisement tells me it can’t help me and I need to communicate with a stateful DHCPv6 server…
R1(config)# interface g0/1
R1(config-if)# ipv6 nd managed-config-flag

## Slide 34: Cisco Router Stateful DHCPv6 Server
DHCPv6
O Flag= x, M Flag = 1
DHCPv6 Server
SOLICIT To all DHCPv6 Servers
3
ADVERTISE Unicast
REQUEST or INFORMATION REQUEST Unicast
REPLY Unicast
4
5
6
The router’s Router Advertisement tells me it can’t help me and I need to communicate with a stateful DHCPv6 server…

## Slide 35: Configuring Stateful DHCPv6
Client IPv6 Address
?

## Slide 36
DHCPv6 Server
Router(config)# ipv6 unicast-routing
Router(config)# ipv6 dhcp pool IPV6-STATEFUL-830
Router(config-dhcpv6)# address prefix 2607:F380:80F:F830:1AB::/80 lifetime infinite infinite
Router(config-dhcpv6)# dns-server 2607:F380:80F:F425::252
Router(config-dhcpv6)# dns-server 2607:F380:80F:F425::253
Router(config-dhcpv6)# domain-name cis.cabrillo.edu
Router(config)# interface GigabitEthernet 0/1
Router(config-if)# ip address 172.20.0.1 255.255.0.0
Router(config-if)# ipv6 address FE80::F830:1 link-local
Router(config-if)# ipv6 address 2607:F380:80F:F830::1/64
Router(config-if)# ipv6 nd managed-config-flag
Router(config-if)# ipv6 dhcp server IPV6-STATEFUL-830
2607:F380:80F:F830::/64
Router Advertisement M=1
DHCPv6 Solicit
DHCPv6 Advertise
The router’s Router Advertisement tells me it can’t help me and I need to communicate with a stateful DHCPv6 server…
G0/1
S
T
A
T
E
F
U
L
D
H
C
P
v
6
Now I have everything I need!

## Slide 37
DHCPv6 Server
2607:F380:80F:F830::/64
Router Advertisement M=1
DHCPv6 Solicit
DHCPv6 Advertise
2607:F380:80F:F830::/64
2607:F380:80F:F830:0:0:0:1
2607:F380:80F:F830:FFFF:FFFF:FFFF:FFFF
2607:F380:80F:F830:1AB::/80
2607:F380:80F:F830:1AB:0:0:1
2607:F380:80F:F830:1AB:0:0:2
2607:F380:80F:F830:1AB:0:0:3 . . .
/64
/80
Reserved for DHCPv6 allocated addresses
Available addresses for this network
2607:F380:80F:F830:1AB::/80
2607:F380:80F:F830:1AB::
G0/1

## Slide 38
DHCPv6 Server
Router(config)# ipv6 unicast-routing
Router(config)# ipv6 dhcp pool IPV6-STATEFUL-830
Router(config-dhcpv6)# address prefix 2607:F380:80F:F830:1AB::/80 lifetime infinite infinite
2607:F380:80F:F830::/64
Router Advertisement M=1
DHCPv6 Solicit
DHCPv6 Advertise
2607:F380:80F:F830:1AB::/80
2607:F380:80F:F830:1AB:0:0:1
2607:F380:80F:F830:1AB:0:0:2
2607:F380:80F:F830:1AB:0:0:3 . . .
/64
/80
G0/1

## Slide 39
Stateful DHCPv6 Server
C:\Users\Student>ipconfig /all
Windows IP Configuration
Ethernet adapter Local Area Connection:
Description . . . . . . . . . . . : Intel(R) 82566DM-2 Gigabit Network Connection
DHCP Enabled. . . . . . . . . . . : No
Autoconfiguration Enabled . . . . : Yes
IPv6 Address. . . . . . . . . . . : 2607:f380:80f:f830:1ab:2de8:cfd8:5e21
Lease Obtained. . . . . . . . . . : Thursday, September 26, 2013 10:17:12 AM
Lease Expires . . . . . . . . . . : Sunday, November 02, 2149 4:45:31 PM
Default Gateway . . . . . . . . . : fe80::f830:1
IPv4 Address. . . . . . . . . . . : 192.168.1.10(Preferred)
Subnet Mask . . . . . . . . . . . : 255.255.255.0
DNS Servers . . . . . . . . . . . : 2607:f380:80f:f425::252
2607:f380:80f:f425::253
Connection-specific DNS Suffix Search List : cis.cabrillo.edu
2607:F380:80F:F828::/64
Router Advertisement
Stateful DHCPv6
2607:f380:80f:f830:1ab:2de8:cfd8:5e21
G0/1
Rest of Interface ID is assigned by the router
show ipv6 dhcp binding

## Slide 40
Stateful DHCPv6 Server
Router# show ipv6 interface g 0/1
GigabitEthernet 0/1 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::F830:1
Description: === Lab network
Global unicast address(es):
2607:F380:80F:F830::1, subnet is 2607:F380:80F:F830::/64
<output omitted>
Hosts use DHCP to obtain routable addresses.
Router#
2607:F380:80F:F828::/64
2607:f380:80f:f830:1ab:2de8:cfd8:5e21
G0/1

## Slide 41: Can a host ignore the Router Advertisement?
DHCPv6
DHCPv6 is similar to DHCPv4.
Host operating systems “may” include the option of ignoring the Router Advertisement from the router and only use the stateful services of a DHCPv6 server.
Note: All addresses should be checked before use with DAD (Duplicate Address Detection), similar to gratuitous ARP in IPv4.
DHCPv6 Server

## Slide 42: Summarize: Router Solicitations and Router Advertisements
Router Advertisement Message
Here is one of three options:
I have everything you need.
I have mostly what you need, but you will need to contact a DHCPv6 server for other information like a DNS address.
I have nothing for you. Contact a DHCPv6 serverl
FF02::1
All IPv6 Devices
Router Solicitation Message
I need IPv6 address information.
FF02::2
All IPv6 Routers
PC1
DHCPv6 Server
1
2

## Slide 43: Final Note
Most ISPs (including Comcast) have quietly turned on IPv6 to the home.
The home router uses DHCPv6 to get it’s ISP-facing IPv6 address.
The home router uses the DHCP-PD (Prefix Delegation) to ask the ISP for an IPv6 network address to give to it’s LAN clients.
The ISP router includes that in it’s DHCPv6 Advertisement.
The home router sends a Router Advertisement message to it’s LAN devices and acts just like a normal IPv6 router:
  SLAAC
  SLAAC + DHCPv6
  DHCPv6 only
Requesting Router
Home Router
Delegating Router
ISP Router
I will be doing another PowerPoint for DHCP-PD

## Slide 44: THANK YOU! 
Rick Graziani - graziani@cabrillo.edu
PowerPoints for CCNA, CCNP, IPv6
  www.cabrillo.edu/~rgraziani
  Username = cisco
  Password = perlman
Shameless plug!
Quality time with my two nieces…

## Slide 45
DHCPv6 and
IPv6 Automatic Address Allocation
Cisco Networking Academy
Rick Graziani
CS/CIS Instructor
Cabrillo College